## Slide 1: Coastal Pioneer Coastal Central Inshore Profiler (CP02PMCI) Data Quality Report
Yuanyuan Xu
University of Delaware
2018-08-01

## Slide 2: Location

## Slide 3: Profiler Dissolved Oxygen

## Slide 4: Deployment Information

## Slide 5: Calibration Information

## Slide 6: Annotations

## Slide 7: Full Time Series of Dissolved Oxygen

## Slide 8: Full Time Series of Pressure

## Slide 9: Quality Control Flag

## Slide 10: Histograms of Full Range Data

## Slide 11: Full Range Profile Time Series

## Slide 12: One week around the changeover

## Slide 13: Comparison Before and After the Redeployment
Before
After

## Slide 14: Narrow down the time range…
Before
After

## Slide 15: Compare with Shipboard Data

## Slide 16: Again, narrow down the time range…

## Slide 17: All Together…

## Slide 18: Conclusions
In general, the dissolved oxygen values during deployment 4 look largely reasonable. There are no major outliers.
The data seems to align with known physical processes, though additional datasets would need to be consulted to confirm. This includes:
  The surface water has higher dissolved oxygen values than the deep water.
  The penetration of the dissolved oxygen decreased in the summer, which is reasonable because of the vertical mixing became weak during the summer.
The profiler was inoperative in the middle of deployment 4, remaining at approximately 30 m depth, however the dissolved oxygen data still appears reasonable. An annotation concerning this is already available in the system.
The profiler dissolved oxygen data agrees generally with a corresponding shipboard CTD cast.
The profiler dissolved oxygen sensor generally work well within half a year. No significant drift is detected in this report.
It is exciting to access OOI data using Python!!